深圳市帕骐电子科技有限公司

新品上架描述表-NA7017B

- Key Features

I720 resolution （1280x720 pixels, horizontal resolution is 1280 TV lines.）

720分辨率（1280×720 Pixels，horizontal resolution is 1280TVLs，对手是900TVLs）

IP69 waterproof rating

IP69级别的防水效果

Our backup camera is made of steel and it won’t be deformed when experiencing external force.

产品由纯铁制成，遭受外力时不易变形。

170°field of view

170°的广角，可视角度达到95%+9+

Reversing view/Usage Scenario

车机上显示的倒车图/场景图

125° adjustable holder

125°可调支架

Stainless steel screws

不锈钢螺丝

Our products are treated against corrosion, quality and durable.

产品本身作了防锈处理，高品质耐用

- Technical Specification

| Image sensor | AHD 1233 1/3 image sensor |
| --- | --- |
| TV system | PAL |
| Effective pixels | 1280H*960V |
| Resolution | HD：1280H*720V |
| Frame rate | 25/30fps |
| S/N ratio | >38[dB] |
| 3D DNR | Support |
| Horizontal resolution | 1280 lines |
| Video output | 1.0VP-P 75 |
| Original/Mirror Image | Original Image |
| Video format | CVBS |
| Angle of lens | 170°wide angle, 100°level angle |
| Auxiliary line | Support |
| Aperture | F=2.0 |
| Lens | F=1.62MM |
| White balance | Auto |
| Exposure | Auto |
| Operating electric current | <100mA |
| Power supply | DC12V |
| Operating temperature | -20 to 70 centigrade, RH 95% Max |

- Package

AV cable

视频连接线

Power cable

摄像头电源线

Mounting screws

安装螺丝包

User manual

说明书