深圳市帕骐电子科技有限公司

产品部-10新品上架描述表

VM1053B

1.Key Features

（Red marked content must be show on Listing Title or Bullet Point ）

- With suction type optical drive: 10.1 inch HD car headrest DVD player will load the disc automatically, easier to change disk for kids and safer to protect loader.

- Built-in full HD decoder: supports multiple 1080P video formats;With HDMI input function, it can sync up to 1080p video from your computer, mobile phone, Raspberry Pi, Xbox or kindle fire etc.

- Adjustable headrest mount holder:With customized headrest mount holder which could hold the DVD player sturdy and firmly,and easy to install in different sizes headrest It’s also allow you to adjust the screen angle for a better viewing angle.

- Built-in FM and IR transmitters,which could transmit audio to car audio via FM or connect to wireless IR Headphones via IR.

- Equipped with a AUX cable:Connect to a car stereo or speaker system for an immersive listening experience.

- Suitable for 12V and 24V vehicles.

- Technical Specification

- screen size: 10.1 Inch

- resolution：1024*600*3RGB LED back light

- speaker power：2*1.8W@1KHZ

- working voltage：DC9-14.4V

- working current：Max power 1.5 A

- video output：75Ω/2Vp-p

- audio output：75Ω/2Vp-p

- THD：1% A weighting （AV output）THD10% （speakers）

- SNR：60db（AV output） 85dB（speakers）

- Laser wavelength：650NM

- working environment：temperature 5-40℃，humidity ＜90%

- net weight: 1275g

- dimensions(LxWxH): 270*178*50mm

- gross weight：2.25kg

- color box size：310*130*225MM

- Instruction

- Package

1* DVD Player

1* Car Charger

1* User Manual

1* Mounting Bracket

1* AUX Cable

1* AV Cable

5.Reference Link

1.产品描述（字体颜色为红色代表要填写在标题或者短描述Bullet Point ）

- 10.1寸高清显示屏头枕DVD播放器，吸入式设计，取放碟片更简便安全

- 全高清1080P视频解码方案，更全面的格式兼容；支持HDMI输入功能，更多的娱乐选择

- 支持视角可调：采用全新可调节头枕安装支架，总会有一个角度适合你的需求；

- 支持FM发射及红外耳机，可将音频通过FM发射至车载音响，或通过IR连接无线IR耳机

- 配备AUX线，可将播放器连接至车机或其他带有AUX-in的放大设备（如音箱、功放等），实现更好音效体验。

- 适用于12V和24V的车型。

2.技术参数

- 屏幕尺寸： 10.1寸

- 分辨率：1024*600*3RGB（LED背光）

- 喇叭功率：2*1.8W@1KHZ

- 工作电压：DC9-14.4V

- 工作电流：MAX POWER 1.5A

- 视频输出：75Ω/2Vp-p

- 音频输出：75Ω/2Vp-p

- 谐波失真：音频输出THD 1% A计权，喇叭输出THD10%

- 信噪比：音频输出 82dbi   喇叭输出 60dbi

- 激光波长：650nm

- 工作环境：温度5-40℃，湿度＜90%

- 单机净重：1275 g

- 尺寸：270*178 *50 mm

- 产品毛重：2.25kg

- 彩盒尺寸：310*130*225 mm

3. 安装/使用说明

4.包装

- 10.1寸吸入式DVD播放机—————————————1；

- 车载电源适配器——————————————————1；

- 说明书（英德西法日意6语合）——————————1；

- 头枕安装支架———————————————————1；

- AV线—————————————————————1

- AUX线————————————————————1

5.参考链接

B07C52ZXWT, B07BNDPTG6