深圳市帕骐电子科技有限公司

产品部-10新品上架描述表

VM1252B

1.产品描述（字体颜色为红色代表要填写在标题或者短描述Bullet Point ）

- 吸入式放碟方式，保护机芯，操作更简单，即使是小孩也可轻松实现取换碟片。

- 采用高品质纠错解码方案，DVD全区支持，还完美兼容VCD,CD等媒体内容，读碟性能更加稳定。

- 采用1366*768 TFT高清屏幕，搭配触摸按键设计；双喇叭设计，给你更好的听觉体验。

- 配备高品质有线耳机，听觉体验全面升级，个人空间尽情享受。

- 支架尺寸可无极调节，适合绝大多数车型尺寸，坚固耐用。

- 配备高品质3M线长的车充，即便7座超长车型，也能轻松连接。配备高识别度遥控器，按键功能一目了然。

2.技术参数

- 屏幕尺寸： 11.6寸(虚标12寸)

- 分辨率：1366*768*3RGB（LED背光）

- 喇叭功率：2*2W@1KHZ

- 工作电压：DC 9-24V

- 工作电流：MAX POWER 1.5A

- 视频输出：75Ω/2Vp-p

- 音频输出：75Ω/2Vp-p

- 谐波失真：音频输出THD 1% A计权，喇叭输出THD10%

- 信噪比：音频输出 82dbi   喇叭输出 60dbi

- 激光波长：650nm

- 工作环境：温度5-40℃，湿度＜90%

- 彩盒尺寸：345*120*255 mm

- 产品毛重：2800g

- 单机净重：1450g

- 尺寸：295*195*55 mm

3. 安装/使用说明

4.包装

- 12寸吸入式DVD播放机—————————————1台；

- 车载电源适配器——————————————————1只；

- 说明书（英德西法意日6语合一） ——————————1本；

- 快速操作指南—————————————————1张；

- 头枕安装支架———————————————————1个；

- AUX线——————————————————— 1根；

- 有线耳机——————————————————— 1个；

- 遥控器（不带电池）——————————————— 1个；

5.参考链接

B077S9YSXB（法国站）

- 电池审核

无内置锂电池以及遥控器电池，无需电池审核，可以走不带电物流。

1.Key Features

（Red marked content must be show on Listing Title or Bullet Point ）

- With suction type optical drive: Car headrest DVD player will load the disc automatically, easier to change disk for kids and safer to protect loader.

- DVD region free: compatible with DVD/SVCD/VCD/CD/MP3/JPG/AVI/AVI/

MPEG/DIVX. Built-in USB/SD card slot (up to 128GB, FAT32).

- 10.1” HD TFT 1366*768 screen with touch button.Dual speaker design,to provide you a better acoustic enjoyment. Equipped with wired headphones can provide enough volume and clear sound quality when watching the movie without any noise effect on others.

- With customized headrest mount holder which can hold the player sturdy and firmly, allows you to adjust the screen angle freely for a better viewing angle and can be used on headrests in different sizes.

- The remote control with highly-recognized buttons make it easy to operate; Customized 9.8 feet cigarette charger to make it much convenient to use even in a 7 - seat car.

- Technical Specification

- Screen size: 11.6 inch TFT screen

- Resolution：1366*768*3RGB LED backlight

- Speaker power：2*2W@1KHZ

- Working voltage：DC9-24V

- Working current：Max power 1.5A

- Video output：75Ω/2Vp-p

- Audio output：75Ω/2Vp-p

- THD：1% A weighting（speakers） 10%（headphones）

- SNR：60db（speakers） 82dB（headphones）

- Laser wavelength：650nm

- Working environment：temperature 5-40℃，humidity ＜90%

- Color box size：345*120*255 mm

- Gross weight：2800g

- Net weight: 1450g

- Product size: 295*195*55mm

- Instruction

- Package

1* 12 Inch Slot-in DVD Player

1* Car Charger

1* User Manual

1* Quick Start Guide

1* Mounting Bracket

1* AUX Cable

1* Wired headphone

1* Infrared Remote Control without battery

- Reference Link

B077S9YSXB（FR）