深圳市帕骐电子科技有限公司

产品部-10新品上架描述表 VM1451B

1.Key Features

- 6-7 Hours Playing Time:Built-in large capacity li-ion battery, supports the player running up to 6-7 hours,so you can enjoy more movies in your trips.14 inch large swivel screen with 1366*768 pixels.

- Region Free DVD Player :Built-in high quality laser, good with error correction, compatible with multiple disc formats.

- Last Memory: Support break-point memory function, and the player will pick up from where you left last time.

- Support USB/SD/MMC Playback: The maximum capacity supported is 128GB.(Note:It needs to be converted to FAT32 format.）

- Support AV Output: With AV cables, you can connect the portable DVD player to larger screens like TV to enjoy a better watching experience.

- Product-friendly: Customized 9.8 feet wall charger and cigarette charger to make it much easier to use.The remote control with highly-recognized buttons make it easy to operate.

- Technical Specification

- Screen size: 14 Inch

- Resolution：1366*768(RGB) LED back light

- Speaker power：2W 8Ω φ40mm（80HZ-18KHZ）

- Working voltage：DC12V

- Working current: 1.5A

- Video output：1Vp-p/75Ω/ NTSC/PAL/AUTO

- Audio output：VP-P2.8V，0DB = 1V 20HZ-20KHZ

- Supported formats：DVD/SVCD/VCD/CD/MP3/JPG/AVI/MPEG/DIVX

- THD：1% A weighting

- SNR：75dB（speakers） 85dB（headphones）

- Laser wavelength：/650NM-795NM

- Battery：7.4VLi ion 5000mAh

- Charging time：more than 6 hours

- Playing time：about 6-7 hours

- Working environment：temperature 5-40℃，humidity ＜90%

- Color box size：388*78*342 mm

- Gross weight：2.4 kg

- Instruction

Please refer to the user manual

- Package

1* DVD Player

1* AC Adapter(3M)

1* Car Power Adapter (3M)

1* Multifunctional Infrared Remote Control

1*φ3.5mm to RCA AV Cable

1* User Manual

- Reference Link

1.产品描述（字体颜色为红色代表要填写在标题或者短描述Bullet Point ）

◆14寸超大可旋转折叠屏幕，分辨率高达1366*768(RGB)；

◆内置大容量锂离子聚合物电池，续航时间可达6-7小时(故事碟中等音量)；

◆采用高品质激光头，支持全区播放，读碟性能更稳定；支持断电记忆功能

◆支持USB/SD/MMC外部存储介质,给你更多娱乐选择。

◆支持AV OUT功能，可连接至其他支持AV IN的设备，如TV等。

◆超实用配件搭配：定制3米长车充和墙充，让设备随时随地使用无忧；高辨识度多功能红外遥控器，使用操作更便捷；

2. 技术参数

- 屏幕尺寸：14 inch

- 分辨率：1366*768（RGB） LED背光

- 喇叭功率：2瓦8Ωφ40mm（80HZ-18KHZ）

- 工作电压：DC12V

- 工作电流：1.5A

- 视频输出：1Vp-p/75Ω/ NTSC/PAL/AUTO

- 音频输出：VP-P2.8V，0DB = 1V 20HZ-20KHZ

- 支持格式：DVD/SVCD/VCD/CD/MP3/JPG/AVI/MPEG/DIVX

- 谐波失真：1% A计权

- 信噪比：75db（喇叭） 85dB（耳机）

- 激光波长：650NM-795NM

- 电池规格：7.4VLi lon 5000MA

- 充电时间：6小时以上

- 播放时间：约6-7小时

- 工作环境：温度5-40℃，相对湿度＜90%

- 彩盒尺寸：388*78*342 mm

- 产品毛重：2.4 kg

3. 安装/使用说明

参照说明书

4.包装清单

- 便携式DVD播放器-------------------------------------------------------------1台；

- 3米长交流电源适配器---------------------------------------------------------1只；

- 3米长车载电源适配器---------------------------------------------------------1只；

- 多功能红外遥控器--------------------------------------------------------------1只；

- φ3.5mm转RCA AV线---------------------------------------------------------1条；

- 使用说明书-----------------------------------------------------------------------1本

5.参考链接