深圳市帕骐电子科技有限公司

VP1057B新品上架描述表

1.产品描述（字体颜色为红色代表要填写在标题或者短描述Bullet Point ）

◆10.1寸TFT高清双屏显示，支持全高清1080P(不支持2K/4K/3DBLU)蓝光碟片播放，让孩子们在旅途中共享美好电影时刻；

◆主机内置4000mAh大容量锂离子电池,支持主机单独持续工作3-4H；同时主机可给副机供电，双屏同时工作可达2-3H;全新主副屏互联方式，让机器运行更加稳定可靠；

◆完全从客户体验角度出发，机器采用翻盖放碟设计，搭配安装绑带装车，无需麻烦的拔线拿出机器即可轻松实现车内取放碟片，且装卸简单，调节方便，适用于不同尺寸的汽车头枕。

- USB和SD卡支持高达1920 * 1080 @ 30fps的高清视频文件播放，可兼容MP4/MKV/MOV/AVI/VOB/FLV/TRP/TS/MPG/MPEG/DAT/ASF/WMV. （未列出的格式暂不支持）。

- 支持：Dolby Digital ,  Dolby Digital Plus,  Dolby TrueHD,    DTS-HD Master Audio MP3等格式Dolby音频解码功能，带给你身临其境的感觉。

- HDMI输出功能，可将高达1080P 60Hz 30fps音视频同步至外界扩展显示设备，如：高清TV等设备。

◆超实用的配件搭配：设计简单且拥有高辨识度按键的遥控，让操作更便捷；

定制的3米长车充和墙充，让你随时随地有备无患。配备专业级AUX线，连接车载音箱，视听体验新升级。

2. 技术参数

- 屏幕尺寸：10.1inch

- 分辨率：1024*600 LED背光

- 喇叭功率：2瓦8Ω（100HZ-15KHZ）

- 工作电压：DC12V

- 工作电流：主机1.5A 副机：0.5A

- 视频输出：1.5Vp-p/75Ω/ NTSC/PAL/AUTO

- 音频输出：VP-P2.8V，0DB = 1V 20HZ-20KHZ

- 支持的碟片格式： BD, BD-R, BD-RE, DVD-R/RW, DVD+R/RW, DVD-Video, VCD, CD, CD-R/RW

- 支持的视频格式：MP4/MKV/MOV/AVI/VOB/FLV/TRP/TS/MPG/MPEG/DAT/ASF/WMV

- 支持的音频格式：Dolby Digital, Dolby Digital Plus, Dolby TrueHD, DTS, WMA, AAC

- 支持的图片格式：JPEG, PNG, GIF

- 谐波失真：1% A计权

- 信噪比：60db（喇叭） 85dB（耳机）

- 激光波长：650NM-795NM

- 电池规格：7.4VLi 4000MAh

- 充电时间：4.5H

- 播放时间：单主机续航时间3-4H，双屏续航时间2-3H

- 工作环境：温度5-40℃，湿度＜90%

- 彩盒尺寸：

- 产品毛重：

3. 安装/使用说明

- 参照说明书

4.包装清单

- 便携式蓝光播放机-------------------------------------------------------------1台；

- 便携式显示器-------------------------------------------------------------1台；

- 交流电源适配器-------------------------------------------------------------1只；

- 车载电源适配器-------------------------------------------------------------1只；

- 多功能红外遥控器-------------------------------------------------------------1只；

- POWER/AV连接线-------------------------------------------------------------1条；

- 使用说明书-------------------------------------------------------------1本；

- 车载头枕固定绑带-------------------------------------------------------------4条；

- AUX线----------------------------------------------------------1条。

5.参考链接

- B076KDH8BV（美国站）B01MTJP163

1.Key Features

- 10.1 inch TFT HD dual screen, support full HD1080P blu-ray discs playback, allows your kids share the same movies on the long trip.(Not support 2K/4K/3DBLU)

- Built-in 4000 mAh large capacity rechargeable battery, the DVD player’s main monitor could support up to 3-4 hrs working time solely, the both monitors could work together for about 2-3hrs.Employ a new connection way between the main and the second monitor to make the devices work more stable and reliable.

- Clamshell design, convenient to change discs with the player mounted. Equipped with 2 mounting straps,convenient to install and adjust in different sizes headrest.

- Support USB/SD/MMC Playback: USB and SD card support up to 1920*1080@30fps HD video file playback, it’s only compatible with MP4/MKV/MOV/AVI/VOB/FLV/TRP/TS/MPG/MPEG/DAT/ASF/WMV.

- Stronger acoustic effect: Supports Dolby audio file decoding, such as: Dolby Digital, Dolby Digital Plus, Dolby True HD, DTS-HD Master Audio MP3, etc, you will feel like you were at the cinema

- With HDMI output and input function, connect to your TV or your mobile phone using a HDMI cable and get digital audio and video transmitted at the highest quality for your movies.(HDMI cable not included.)

- The remote control with highly-recognized buttons make it easy to operate; Customized 9.8 feet wall charger and cigarette charger to make it much easier to use.Equipped with a 6.6 feet AUX cable: Connect to car stereo or speaker system for an immersive experience.

- Technical Specification

- Screen size: 10.1 Inch

- Resolution：1024*600 LED backlight

- Speaker power：2W 8Ω φ28mm（80HZ-18KHZ）

- Working voltage：DC12V

- Working current：Main player 1.5 A  Monitor 0.5A

- Video output：1.5Vp-p/75Ω/ NTSC/PAL/AUTO

- Audio output：VP-P2.8V，0DB = 1V 20HZ-20KHZ

- Supported disc formats：BD, BD-R, BD-RE, DVD-R/RW, DVD+R/RW, DVD-Video, VCD, CD, CD-R/RW

- Supported video formats：MP4/MKV/MOV/AVI/VOB/FLV/TRP/TS/MPG/MPEG/DAT/ASF/WMV

- Supported audio formats：Dolby Digital, Dolby Digital Plus, Dolby TrueHD, DTS, WMA, AAC

- Supported image formats：JPEG, PNG, GIF

- THD：1% A weighting

- SNR：60db（speakers） 85dB（headphones）

- Laser wavelength：/650NM-795NM

- Battery：7.4VLi ion 4000MA

- Charging time：4.5 hours

- Playing time：the main player can keep running for 3-4 hrs, or the both monitors could work together for about 2-3 hrs.

- Working environment：temperature 5-40℃，humidity ＜90%

- Product dimension:mm

- Color box size:mm

- Gross weight:kg

- Instruction

Please refer to the user manual

- Package

1* DVD player

1* LCD monitor

1* AC Adapter

1* Car Charger

1* Infrared Remote Control

1* Power/ AV Cable

1* AUX Cable

1* User Manual

2* Headrest Strap

5.Reference Link

- B076KDH8BV（US）B01MTJP163