深圳市帕骐电子科技有限公司

产品部-10新品上架描述表

1.Key Features

（Red marked content must be show on Listing Title or Bullet Point ）

产品描述（字体颜色为红色代表要填写在标题或者短描述Bullet Point ）

- Android 4.4 Kit Kat, CPU: Rockchip PX3 Cortex A9 Quad Core 1.6GHz, RAM: 2GB, Optimized Radio IC:NXP TEF6686,

安卓4.4操作系统，四核CPU，运行内存2GB，高品质的收音IC:NXP TEF6686

- 3D DSP Sound Effect will enhance your music. Support Extreme Bass,Simply turn on the 3D surround effect, you'll experience a new virtual surround sound feeling from the built-in 3D DSP processor.

DSP音效增强你的音乐效果，支持超重低音,打开3D 环绕声效，你会从机子内置的DSP处理器里面体验到一个全新的虚拟的环绕立体声。

- GPS Navigation(map software or app not included), Built in USB Port/ Micro SD Slot (up to 64GB),  WIFI(Built in WIFI modem)/3G(Extra device required), Cam-In(Extra device required)

GPS功能，内置USB/SD卡槽（最大支持64GB），内置wifi模块，支持3G网络（要求额外的设备），支持倒车摄像头功能（摄像头选配）

- Please compare the dimensions, shape of this unit with the central console before purchasing, in case it does not fit the size.

购买前请先核对机子的形状和尺寸

- Support Bluetooth phone call / audio player/ Phone Book function，support external mic.

支持蓝牙通话，蓝牙音乐，支持同步电话本和支持外置麦克风

- Technical Specification技术参数

Item Description:

6.2" Touchscreen Android 4.4 Quad Core 1.6GHz DSP Car DVD Player with RAM:2GB

Attention: Please check the dimension of this unit before purchasing，and we only provide universal ISO cable

Specifications：

General:

OS: Android 4.4 Kit Kat

CPU: RK3188 Cortex A9 Quad Core 1.6GHz

RAM: DDR3 2GB

Nand Memory: 16GB

Audio output: 4*45W max

Screen Resolution: 800*480

Cold Boot time: about 25-35s

Screen:

Screen Size: 6.2-Inch Digital Screen

Resolution: 800*480

Capacitive Touch Screen (5 points)

Image Brightness /Contrast/ Color Adjustable

GPS：

Map Storage Mode: micro SD card

Voice Guidance: Yes (Include most Languages)

3D Map: Yes

POI Display: Yes

GPS Communication Port: Auto Search and connect

DVD:

DVD drive: Region Free

Compatible Formats:

AVI/DVD/DVD+R/DVD-R/DVD+RW/DVD-RW/VCD/MP3/CD/CD-RW/JPEG etc.

Support Dual Zone

Support radio/disc/Bluetooth/USB/SD playback while navigating.

Bluetooth:

Built-In Microphone in the control panel for hands free calling function

Support External microphone clear voice calling

Support Bluetooth audio player/Phone Book function

(Attention: This function can only be realized when the mobile phone supports Bluetooth Audio Output/Contacts Output)

Support Bluetooth Connection for iPhones/ Most Android Phones/ Even some None Smart Phone

(Attention: The Bluetooth just for audio stream transfer, it doesn’t support file transfer or Internet tethering.)

Steering Wheel Control

Change the track, volume, etc. conveniently without taking your hands off the steering wheel, which makes your driving much safer.

(Attention: Only support resistance based analog input steering wheel.)

Radio:

Good quality radio IC: NXP TEF6686 ,with good radio reception.

AM/FM tuner built in (worldwide)

AM frequency range: 522-1620 (Europe), 530-1710 (America), 522-1620 (Russia)

FM frequency range: 87.5-108 (Europe), 87.5-107.9 (America), 65.0-108.0 (Russia)

RDS Radio: Yes

USB/SD:

Built in USB Port/ Micro SD Slot

Micro SD Card Slot/ USB Port: Can support micro SD Card /USB drive up to 64GB with FAT32 or ntfs format

Support Audio Formats: MP3/WMA/WAV/APE/FLAC/ACC/OGG/AC3, etc.

Support Video Formats: RMVB/AVI/MPG/MPEG/WMA/VOB/MOV/ASF/FLV/3GP/MP4, etc.

EQ

Max audio output: 4 X 45W ,

Signal-To-Noise Ratio:>55db

DSP Subwoofer：

3D DSP Sound Effect will enhance the enjoyment of music.

Support Extreme Bass,Just turn on the 3D surround effect,

you'll experience a new virtual surround sound feeling from the

built-in 3D DSP processor.

OSD Language:

English, Russian, Spanish, Turkish, Portuguese, Arabic, farsi，

Italian, German, French, Ukrainian，Romanian，Indonesian，Vietnamese，

Thai, Hebrew, Hungarian，Polish，Greek，Bulgarian

WIFI/3G(Extra device required)

3G: Require external USB 3G modem (Search Y0014 on our store) and your local Internet SIM card to be connected

Support WCDMA/CDMA2000/TD-SCDMA 3G bandwidth

WIFI: Built in WIFI modem

Direct turn on WIFI function to search and connect to any free WIFI hotspots

Cam-In(Extra device required)

Support RCA type reverse camera input,

Automatically trigger to reverse camera when reverse the car

- Instruction 使用说明

- Package包装

5.Reference Link参考链接