深圳市帕骐电子科技有限公司

新品上架描述表-NA7011B

- Key Features

Infrared backup camera with built-in SONY CCD sensor & Wide View Angle enable you to have a bright and clear night vision while driving. 红外后视摄像头，内置SONY CCD感光元件。宽视角（不用标明多少度），夜视清晰明亮。

IP69 Waterproof level allows it to work in great condition even in pouring rain and violent storm, so you don’t need to worry about fog or water intrusion.IP69的防水级别使其能在大雨和风暴中正常工作。不必担心进雾或进水。

7-in LCD TFT Monitor Screen with an 800*480 high resolution and 2 video inputs. One of them is for reversing view, the other is for front view. (not include) 7寸LCD TFT的显示器屏幕，800*480高清分辨率，2路视频输入。一路后视，一路前视 (不包括)。

When reversing the car, the monitor will automatically turn to reversing video. Meanwhile, Built-in microphone enables you to hear the sounds at the rear.在你倒车的时候，屏幕上的画面会自动跳转都后视镜头所拍摄到的画面。内置麦克风能让你清晰地听到车尾的声音。

Perfect Night Vision and your best night drive company. With its high quality LCD TFT display and infrared backup camera, you do not have to worry about color fade issue. And the blue button light makes operating more fluently under low lighting conditions.绝佳的夜视效果是你夜晚驾车的好伙伴。有了高质量的LCD TFT显示屏和红外后镜头，不用担心出现偏色问题。蓝色按键灯，在光源微弱的情况下也能操作自如。

Perfect for large vehicles such as trailers, trucks, RVs, etc.适用于拖车，卡车，房车等大型车辆。

参考标题

主图标题：BACKUP CAMERA & 7" LCD TFT MONITOR

CCD对比标题：Image Sensor Comparison: Sony CCD sensor & Other CCD sensor

夜视标题：Night Vision

防水标题：IP69 waterproof& Wide Angle FOV

2路输入标题：2 Video Inputs. One for reversing view, one for front view.

装车实景标题：Usage Scenario

布线图：Installation positions

配件图：What’s in the box

- Technical Specification技术参数

- MONITOR

Display: Color TFT-LCD

Size: 7” (Diagonal)

Resolution: 800 x 480

Color System: PAL/NTSC/AUTO /SEVAM

AV Channels: 2 (4 Pin Aviation)

Power: 12-24Volts DC

Connector Plug: Male Screw Plug

Mounting Bracket: Metal U type

Buttons: Illuminated

Operating Temp: -20℃to +70℃

Remote Control: Yes (IR)

OSD Menu: Yes

Audio: Yes

- Camera

Sensor: 1/3 CCD

Sensitivity: 0 Lux with IR

Electronic Shutter: Auto

Lens: f 2.9mm

AGC: Auto

Power: 12 volt DC

Operating Temp: -20℃ to +70℃

Plug: 4 Pin Aviation

Audio: No

- AV CABLE

Length: 20m

Connector Type: 4 Pin Male / 4 Pin Female

Connector: Aviation Type

What’s in the box

7” TFT LCD Monitor

IR CCD Camera with Sun Hood and Bracket

2m Power Cable

U Type Monitor Bracket

Removable Sun Hood

20m AV Cable

Mounting Screws

IR Remote Control

User Manual

Mounting Stand

参考商品：

B079BSVTYW

B0753DPCXK

B073Q4JJ3Z